Utilizing artificial neural networks for Ethernet II error correction.
Marek Szymański, Mateusz Nurczyński

# Abstract
Based on the assumption, that live Internet communication is, in it’s nature, self-similar, we asserted that it is possible to build a machine learning model, that would identify and correct errors in Internet transmissions.
Currently there are no error correction methods in use, that would attempt to employ a statistical model analyzing the very data being transmitted.
To verify the basic assumptions of this hypothesis (that self-similarity of the Internet traffic can be recognized by a machine learning model and used to correct errors), we attempted to train an artificial neural network model to correct single-bit errors in Ethernet II frames captured from live Internet traffic.
<here we will describe our results once we have them>

# Introduction
## Self-similar Internet
Self-similar nature of the Internet traffic has been demonstrated by multiple researchers: ,,We also find a notable self-similarity feature of the autocorrelations in the data and its aggregates, in all the cases studied.”[1].
[1] D. Chakraborty, A. Ashir, T. Suganuma, G. Mansfield Keeni, T. K. Roy, N. Shiratori ,,Self-similar and fractal nature of Internet traffic”
I’s also been found, that Ethernet traffic demonstrates some degree of fractal nature: ,,the critical characteristic of this self-similar traffic is that there is no natural length of a "burst": at every time scale ranging from a few milliseconds to minutes and hours, similar-looking traffic bursts are evident”[2]
[2] W. E. Leland, M. S. Taqqu, W. Willinger, D. V. Wilson ,,On the self-similar nature of Ethernet traffic”
Such finding are not surprising, since across all abstraction layers there is a limited number of Internet protocols in wide use, which naturally leads to certain elements (like headers of high-level protocols or even payloads of widely used network applications) repeating frequently in transmissions.
## Possible implications for error correction
However, the possibility of building a statistical model based on those characteristics have never been explored as a possible way to identify transmission errors.
Even within a single Ethernet frame there is a multitude of dependencies across all network abstraction layers. For example, information provided in an HTTP header (like language and file type) will correspond with the payload.
We asserted, that those dependencies could be used to build a deep learning model, that would allow to correct network transmission errors.
We performed a series of tests on live Ethernet II traffic, attempting to train artificial neural networks of various sizes, architectures for correcting single-bit transmission errors. The purpose was to verify whether this method of error correction is at all feasible.
This document is a synthesis of all our findings.

# Methods
Below we outline in great detail how we performed the aforementioned tests.
## Data gathering and preparation
Below is a description on how we gathered and transformed the data for our model.
### Capturing
We collected the data for our analysis using version 4.0.8 of open-source Wireshark software, running on a 64-bit x86 machine under a Unix-based operating system (Fedora Linux Workstation 37). All communication was captured in a small 1Gb Ethernet LAN network, while the computer was being used normally.
We captured over 220 000 Ethernet II frames of various sizes and payloads. We could only capture valid (non-damaged) frames and without their CRC check-sum.
### Filtering
Since our purpose was to verify whether this way of error correction is at all feasible, we decided to simplify the problem by only including frames carrying IPv4 packets (210 000 out of 220 000 frames).
### Address randomization
All of our frames had the same two MAC addresses in them, as well as a subset of similar IP addresses. In order to avoid contaminating the model with that information, we decided to randomize all MAC and IP addresses in our data.
### Cyclic Redundancy Check (CRC)
CRC is the check-sum used for Ethernet II frames.[3] Due to the limitations of the capturing setup we were only able to capture the Ethernet frames without that check-sum. Therefore, we decided to compute the CRC32 (0xEDB88320) check-sum ourselves and add it to all of the frames.
[3] T. Schmidt ,,CRC Generating and Checking”
### Encoding
In order to imitate the way transmission errors are introduced into frames in real-life conditions we decided to run 8b/10b encoding[4], introduce single-bit errors into the encoded frames and then decode them.
[4] S. Yaday, S. Pandey A. Gupta ,,Implementation of 8B/10B encoder-decoder for Gigabit Ethernet Frame”
### Introducing errors into the frames
We introduced at least one error into each frame, and each frame had a 0.1 chance of a second error being introduced. All errors were put on random positions within the frames.
### Buffering and CRC position change
All frames that were below maximum size had to receive a buffer of zeroes at the end in order to fit into the fixed-size input layer of a neural network. Since the check-sum could be useful for our model to correct the error, we wanted it to be place at the same position, not matter the frame size. Therefore, after decoding, we put it at the end of the buffer, instead of immediately at the end of the frame:
Frame header and payload	Buffer (zeroes)	CRC